CURRICULUM EMBEDDED PERFORMANCE TASK MATRIX—NINTH GRADE HIGH SCHOOL SCIENCE (CAPT)

| PARAMETER | GRADE 9 STRAND I: ENERGY TRANSFORMATIONS |
| --- | --- |
| EMBEDDED TASK TITLE | SOLAR COOKER |
| YOUR TASK | You and your lab partner will design and conduct an experiment to investigate one factor that contributes to the effectiveness of solar cooker in heating water. Factors you may want to investigate include: the shape of the collector, the shape of the water container, orientation of the collector, surface area of the collector, or the color of the collector. |
| RESEARCH QUESTION | Of black (≈ tar), brown (≈ soil), green (≈ vegetation), and beige (≈ sand) which color solar cooker will have the highest final temperature? |
| HYPOTHESIS/PREDICTION | If black, brown, green, and beige lined solar cookers are subjected to direct sunlight, then the black solar cooker will have the greatest increase in temperature because black absorbs the most energy. |
| EXPERIMENT INDEPENDENT VARIABLE | The color (black, brown, green, and beige) of the paper lining the solar cooker. |
| EXPERIMENT DEPENDENT VARIABLE | The increase in temperature of the water in (C. |
| CONTROL EXPERIMENT | Instead of colored construction paper line the solar cooker with white construction paper. |
| VARIABLES THAT MUST BE KEPT CONSTANT | Shape and size of the solar collector, orientation of the solar cooker toward the sun, surface area of the colored paper inside the solar cooker, angle of the solar collector to the sun (i.e., 90() same reflective surface (aluminum foil), and the same thickness of Saran Wrap to let the light into and trap the heat. |

A Typical Solar Cooker

Solar Cooker

Student Materials

Most people in the United States use an electric stove or a natural gas stove to cook their food.  This is not the case in much of the world.  Approximately 50% of the people on Earth cook using fire from burning wood.  However, due to overuse, wood is becoming a scarce commodity in many countries.  In addition, burning wood is a major source of air pollution.

One alternative to cooking with wood is using solar cookers.  These devices use energy from the sun to cook food without producing any pollution.  While there are many designs for solar cookers, a simple solar cooker can be made from everyday materials.  There are many factors that can influence the effectiveness of a solar cooker including the size of the collector, the orientation of the panel and the color of the container.

Learning objective:

Students will be able to use solar energy to heat water and understand the design factors that influence the effectiveness of capturing solar energy in this context.

You have been provided with the following materials and equipment.  It may not be necessary to use all of the equipment that has been provided.

Suggested materials:

Heat lamps or sunlight			Tape

Cardboard 				Thermometer

Aluminum foil				Water

Container for water			White, black, green, and beige construction paper

Safety goggles

INITIAL TEMPERATURE OF THE WATER = 20( C (68( F)

Temperatures of the Heated Water ((C) in the Solar Cooker

| (Independent Variable) Color of Paper | Initial (Starting) of the Water in the Solar Cooker ((C) | Trial #1 (Dependent Variable) Final Temp of the Water ((C) | Trial #2 (Dependent Variable) Final Temp of the Water ((C) | Trial #3 (Dependent Variable) Final Temp of the Water ((C) | 3 Trial Average (Dependent Variable) Final Temp of the Water ((C) | Increase in Water Temp ((C) |
| --- | --- | --- | --- | --- | --- | --- |
| Control Experiment White Construction Paper | 20 | 24 | 25 | 26 | 25 | 5 |
| Black Construction Paper | 20 | 72 | 79 | 74 | 71 | 51 |
| Brown Construction Paper | 20 | 57 | 56 | 52 | 55 | 35 |
| Green Construction Paper | 20 | 49 | 48 | 47 | 48 | 28 |
| Beige Construction Paper | 20 | 42 | 38 | 40 | 40 | 20 |

QUESTIONS

- Use the graph and data table to describe the relationship between color of the solar cooker and the increase in temperature.

- Was the hypothesis (prediction) supported? Explain!

- Write the procedure to carry out this experiment.

- Why does the white solar cooker heat up at all?

- In terms of validity why is the 3 trial average better than a single trial?

- Use the graph and data table to answer the following question:

If you were stuck outside on a brutally hot, sunny, summer day which place would be

the coolest in terms of a spot to hang around; [1] a parking lot made of tar, [2] a

plowed field with no crops, [3] a grassy field, or [4] the beach. Explain!

- Identify 5 variables that were held constant in the solar cooker experiment.

- Explain why it is important for these variables to be held constant.

- If you want to cook a frozen pizza using the sun which color solar collector would cook this delight the fastest?